## Slide 1
MIPS Assembly Programming
From your first 'Hello World' to recursive functions on the stack
Hanyang University ERICA Campus
Department of Robotics - Computer Architecture
Instructor: Prof. Bumjin Jang
Zhuoheng Li
lzh9768@hanyang.ac.kr
MIPS Assembly - Computer Architecture, Hanyang ERICA

## Slide 2
MARS: Our Simulator
MIPS Assembler and Runtime Simulator (Java, free)
▸ Edit - syntax-highlighted .asm editor, multi-file support
▸ Assemble (F3) - translates your code to machine code, reports syntax errors
▸ Run (F5) - execute the program; output shows in the bottom Run I/O pane
▸ Step (F7) - single-step through each instruction
▸ Inspect - live view of all 32 registers and main memory while you step
▸ Help - built-in syscall reference (Help -> Syscalls)
Download: https://dpetersanderson.github.io/ (requires Java)
MARS Simulator

## Slide 3
MARS Anatomy
Four panels you will use constantly
1. Edit / Execute Tabs
Edit shows your source.
Execute shows assembled machine code.
2. Code Editor
Type and edit your .asm file here.
Line numbers, syntax colours.
3. Registers Panel
All 32 GP registers + HI / LO + PC.
Values update as you step.
4. Run I/O
syscall 4 / 1 prints appear here.
syscall 5 / 8 reads input here.
MARS Anatomy

## Slide 4
General-Purpose Registers
32 registers, named by role - learn the convention, not the number
Name
Number
Purpose
$zero
$0
always 0 (cannot be written)
$at
$1
assembler-temporary - do not touch
$v0 - $v1
$2-$3
function return values, also syscall code in $v0
$a0 - $a3
$4-$7
function arguments (and syscall arguments)
$t0 - $t9
$8-$15, $24-$25
temporaries - caller-saved (free for any use)
$s0 - $s7
$16-$23
saved registers - callee MUST preserve them
$gp / $sp / $fp
$28-$30
global / stack / frame pointer
$ra
$31
return address (set automatically by jal)
General-Purpose Registers

## Slide 5
Floating-Point Registers (Coprocessor 1)
Separate file: $f0 - $f31, used by all FP instructions
▸ 32 single-precision regs - $f0 through $f31 - hold 32-bit floats
▸ Doubles use a PAIR - $f0/$f1, $f2/$f3, ... - always even/odd
▸ Argument convention - $f12 receives the float / double for print syscalls
▸ Return convention - $f0 holds the result for read-float / read-double syscalls
▸ Move between FP regs - use mov.s (single) or mov.d (double), NOT 'move'
▸ Load / store - lwc1 / swc1 for floats; l.d / s.d for doubles
Floating-Point Registers

## Slide 6
Anatomy of an .asm File
Two sections, one syscall pattern - every program looks like this
.data # variables / constants live here
msg: .asciiz "Hello!" # null-terminated string
.text # instructions live here
li $v0, 4 # service code 4 = print string
la $a0, msg # argument: address of the string
syscall # ask the OS to do it
li $v0, 10 # service code 10 = exit
syscall # clean termination
Pattern: load syscall code into $v0 -> load arguments -> syscall
Anatomy of an .asm File

## Slide 7
Lesson 3 - Print a String (syscall 4)
.data
msg: .asciiz "Hello World!"
.text
li $v0, 4 # 4 = print string
la $a0, msg # address of the string
syscall
li $v0, 10 # 10 = exit
syscall
Key ideas
.asciiz stores text + a 0 byte at the end.
li loads an immediate (constant) into a register.
la loads the ADDRESS of a label - not the value.
syscall hands control to the OS to actually print.
Output: Hello World!
Lesson 3 - Print a String

## Slide 8
Lessons 4 & 5 - Print Character / Integer
Same pattern, different syscall
Print a Character
# syscall 11 = print one character
li $v0, 11
li $a0, 'A' # ASCII 65
syscall
li $v0, 10
syscall
Print an Integer
# syscall 1 = print signed 32-bit int
li $v0, 1
li $a0, 42
syscall
li $v0, 10
syscall
syscall code in $v0 + argument in $a0 -> syscall
Lessons 4 & 5 - Print Character / Integer

## Slide 9
Lessons 6 & 7 - Print Float / Double
FP arguments live in $f12 (and $f13 for doubles)
Float (32-bit, syscall 2)
.data
pi: .float 3.14159
.text
li $v0, 2 # print float
lwc1 $f12, pi
syscall
Double (64-bit, syscall 3)
.data
pi: .double 3.141592653589793
.text
li $v0, 3 # print double
l.d $f12, pi # loads $f12 + $f13
syscall
Doubles ALWAYS occupy a pair: $f12 + $f13, $f20 + $f21, ...
Use 'lwc1' for floats and 'l.d' for doubles - do NOT use plain 'lw'
Lessons 6 & 7 - Print Float / Double

## Slide 10
Lessons 8 & 9 - Add and Subtract
Load operands -> compute -> print
.data
num1: .word 30
num2: .word 12
.text
lw $t0, num1 # $t0 = 30
lw $t1, num2 # $t1 = 12
add $t2, $t0, $t1 # -> 42 (Lesson 8)
sub $t3, $t0, $t1 # -> 18 (Lesson 9)
li $v0, 1 # print int
move $a0, $t2 # ('move' = pseudo for 'add ..., $zero')
syscall
All R-type arithmetic has the same shape: op rd, rs, rt
Lessons 8 & 9 - Add and Subtract

## Slide 11
Lessons 10 & 11 - Multiplication: mul vs mult
Pseudo-instruction (easy) versus the real hardware (precise)
Lesson 10 - mul (pseudo)
# 'mul' - PSEUDO, 3 operands
# Result goes directly into $t2.
# Convenient if the answer fits in 32 bits.
mul $t2, $t0, $t1 # $t2 = $t0 * $t1
Lesson 11 - mult (real)
# 'mult' - REAL, 2 operands
# Result is 64 bits, split across HI:LO.
mult $t0, $t1
mflo $t2 # low 32 bits
mfhi $t3 # high 32 bits
100000 * 50000 overflows 32 bits -> use mult + mfhi/mflo to keep the upper word
Rule of thumb: prototype with 'mul', switch to 'mult' when correctness matters
Lessons 10 & 11 - mul vs mult

## Slide 12
Lesson 12 - Multiply via Shift (sll)
When the multiplier is a power of two, shifting is much faster
lw $t0, num # $t0 = 5
sll $t1, $t0, 3 # $t1 = 5 << 3 = 5 * 2^3 = 40
# General rule: x << n == x * (2^n)
Bit picture
5 = 0000 0000 0000 0000 0000 0000 0000 0101
5 << 3 = 0000 0000 0000 0000 0000 0000 0010 1000 ( = 40 )
Each left shift inserts a 0 on the right -> value doubles.
3 left shifts -> multiplied by 2 * 2 * 2 = 8.
Lesson 12 - Multiply via Shift (sll)

## Slide 13
Lessons 13 & 14 - Division
Symmetric to multiplication: pseudo gives quotient, real gives both
Lesson 13 - pseudo (quotient only)
# 'div' - PSEUDO, 3 operands
# Stores ONLY the quotient.
div $t2, $t0, $t1
# 17 / 5 -> $t2 = 3
Lesson 14 - real (quotient + remainder)
# 'div' - REAL, 2 operands
# LO = quotient, HI = remainder.
div $t0, $t1
mflo $t2 # quotient = 3
mfhi $t3 # remainder = 2
When you need BOTH quotient and remainder, the real instruction is the only choice
Mnemonic: mfLO -> quotient (Lower) mfHI -> remainder (Higher leftover)
Lessons 13 & 14 - Division

## Slide 14
Why HI and LO?
Two special 32-bit registers that hold mult / div results
▸ Outside the 32 GP registers - you cannot use them as direct operands
▸ mult writes both - HI = upper 32 bits, LO = lower 32 bits of a 64-bit product
▸ div writes both - HI = remainder, LO = quotient
▸ Read with mfhi / mflo - 'move from HI / LO' into a normal register
▸ Why a separate file? - they're wide enough for the 64-bit result without changing the ISA
Forgetting mflo / mfhi is the #1 reason 'my multiply does nothing'
HI and LO Registers

## Slide 15
Lesson 15 - Functions with jal / jr
Two instructions are all you need to call and return
.data
msg: .asciiz "Hello from a function!"
.text
main:
jal greet # call greet(); $ra <- ret addr
li $v0, 10 # exit when we come back
syscall
greet:
li $v0, 4
la $a0, msg
syscall
jr $ra # return to caller (main)
Mental model
jal LABEL
- jump to LABEL
- AND copy the address
of the next instruction
into $ra
jr $ra
- jump to whatever
address $ra holds
Together: function call.
Lesson 15 - Functions with jal / jr

## Slide 16
Lesson 16 - Arguments and Return Values
MIPS calling convention: $a0-$a3 in, $v0-$v1 out
.text
main:
li $a0, 5 # 1st argument
li $a1, 7 # 2nd argument
jal addTwo # result lands in $v0
move $a0, $v0 # forward to print syscall
li $v0, 1
syscall
li $v0, 10
syscall
addTwo:
add $v0, $a0, $a1 # $v0 = $a0 + $a1
jr $ra
Convention
Caller side
- put args in $a0, $a1, ...
- jal target
- read result from $v0
Callee side
- use $a0..$a3 as inputs
- put result in $v0
- jr $ra to return
Lesson 16 - Arguments and Return Values

## Slide 17
The Stack
A LIFO scratch space, addressed through $sp
▸ $sp = stack pointer - always points to the lowest used byte
▸ Stack grows DOWNWARD - to push, SUBTRACT from $sp
▸ To pop, ADD back to $sp - after reading the value
▸ Each slot is 4 bytes - for word-aligned data; align to 8 for doubles
(higher addresses)
caller's data
$ra (saved)
$a0 (saved)
<- $sp
(lower addresses,
stack grows here)
Push: addi $sp, $sp, -4 ; sw $reg, 0($sp) Pop : lw $reg, 0($sp) ; addi $sp, $sp, 4
The Stack

## Slide 18
Lesson 17 - Saving Registers to the Stack
$s0-$s7 are callee-saved: a function MUST preserve them
clobber:
addi $sp, $sp, -4 # allocate 4 bytes (PUSH)
sw $s0, 0($sp) # save caller's $s0
li $s0, 999 # callee uses $s0 freely
lw $s0, 0($sp) # restore caller's $s0 (POP)
addi $sp, $sp, 4 # free the stack space
jr $ra
If you forget to restore $s0, the CALLER will see 999 instead of 100
$t0-$t9 are caller-saved -> the caller must save them if they care after a call
Lesson 17 - Saving Registers to the Stack

## Slide 19
Lesson 18 (Part 1) - Why Nested Calls Need the Stack
The inner 'jal' overwrites $ra - so the OUTER caller MUST save it first
▸ Single call? - $ra survives - nothing else writes to it
▸ A function calls another? - the inner jal CLOBBERS $ra
▸ Solution - outer function pushes $ra on the stack BEFORE the inner call
▸ Same for $a0 - if you'll need the argument again after the call, save it too
▸ Recursion - is just a function calling itself - same rule applies
Allocate ONE stack frame at the top of the function, free it before EVERY return path
Lesson 18 (Part 1) - Why Nested Calls Need the Stack

## Slide 20
factorial(3) - Stack Walkthrough
Each call gets its own slot for $ra and n
Call sequence
main calls factorial(3)
factorial(3) pushes $ra,3 then calls factorial(2)
factorial(2) pushes $ra,2 then calls factorial(1)
factorial(1) returns 1 (base case)
factorial(2) pops $ra,2 returns 1 * 2 = 2
factorial(3) pops $ra,3 returns 2 * 3 = 6
main receives 6 in $v0
Stack at deepest call
n = 3
$ra (main)
n = 2
$ra (fact 3)
n = 1 (base)
<- $sp
factorial(3) - Stack Walkthrough

## Slide 21
Lesson 18 (Part 2) - Recursive Factorial Code
factorial:
addi $sp, $sp, -8 # reserve two slots
sw $ra, 0($sp) # save return address
sw $a0, 4($sp) # save n
slti $t0, $a0, 2 # n < 2 ?
beq $t0, $zero, recurse
li $v0, 1 # base: factorial(0)=factorial(1)=1
addi $sp, $sp, 8
jr $ra
recurse:
addi $a0, $a0, -1
jal factorial # $v0 = factorial(n - 1)
lw $a0, 4($sp) # restore n
lw $ra, 0($sp) # restore $ra
addi $sp, $sp, 8
mul $v0, $v0, $a0 # $v0 = factorial(n-1) * n
jr $ra
Lesson 18 (Part 2) - Recursive Factorial Code

## Slide 22
Lessons 19 - 21 - Reading Numbers
syscall 5 / 6 / 7 = read int / float / double
Code
Reads
Result lands in
Save it!
syscall 5
read integer
result in $v0
move $t0, $v0
syscall 6
read float
result in $f0
mov.s $f20, $f0
syscall 7
read double
result in $f0/$f1
mov.d $f20, $f0
Always SAVE the result before the next syscall - any syscall may reuse $v0 / $f0
Lessons 19-21 - Reading Numbers

## Slide 23
Lesson 22 - Reading a String (syscall 8)
Reserve space yourself - the OS won't allocate for you
.data
prompt: .asciiz "Enter your name: "
greeting: .asciiz "Hello, "
buffer: .space 64 # 64 bytes of zero memory
.text
li $v0, 4
la $a0, prompt
syscall
li $v0, 8 # read string
la $a0, buffer # where to put it
li $a1, 64 # max bytes (incl trailing 0)
syscall
li $v0, 4
la $a0, greeting
syscall
li $v0, 4
la $a0, buffer # buffer is null-terminated -> printable
syscall
Lesson 22 - Reading a String

## Slide 24
Resources
Everything is open-source and on GitHub
Tutorial videos
Amell Peralta
MIPS Assembly Programming Simplified
(YouTube playlist)
Simulator
MARS - MIPS Assembler
and Runtime Simulator
https://dpetersanderson.github.io/
Source code
github.com/lizhuoh9/MIPS-Assembly
20 worked examples,
lessons 3 - 22
Recommended: clone the repo, open MARS, run each lesson while you watch the video.
Resources

## Slide 25
Thank You
Questions?
github.com/lizhuoh9/MIPS-Assembly
Q&A